## Slide 1: Introduction of Math of MBD
2022/04/06
Graham Sanborn
Part 1: MBD Equations of Motion
Copyright © 2022 FunctionBay, Inc. All rights reserved.
FunctionBay, Inc. R&D Group.

## Slide 2: Overview
Goal
  Introduce the mathematics of Multibody Dynamics
3 Parts:
  MBD Equations of Motion
  Solving the Equation of Motion
  Special Features
    Contact
    Flexible bodies

## Slide 3: Presentation Parts
MBD requires 2 parts:
  Equations of motion
    f = ma
  The solution to the equations of motion
    time stepping
The third part extends MBD’s capabilities.
  Flexible bodies and contact

## Slide 4: Part 1:
MBD equations of motion

## Slide 5: Body Dynamics
Dynamics of a rigid body
  Every body has a position and an orientation.
  Consider a body (Body i) in 2 dimensions
    It has 3 coordinates:
      xi = [xi, yi]T : Position of the center of mass
      θi: Orientation
Body i
Body i in the global reference frame
x
y
xi
θi

## Slide 6: In this Seminar, 2D Only
In this seminar, we will only consider 2D.
3D rotation is complex.
  There are many details, equations, considerations.
The fundamental MBD concepts are the same for 2D and 3D.
  Rotation should be studied after the fundamental concepts are fully understood.

## Slide 7: Body Dynamics
Body coordinates, velocities, and accelerations
Body coordinates
Body velocities
Body accelerations
x
y
xi
θi
xi : location of center of mass (CM) of Body i

## Slide 8: What is MBD?
What is Multibody Dynamics (MBD)?
  Motion of a system of connected bodies
What is “motion”?
  Motion = position, velocity, and acceleration, over time
  Mathematics of motion = the “equations of motion”
    Really, the acceleration equations.
  MBD starts from the acceleration equations of acceleration of a single rigid body.
translation
rotation

## Slide 9: Rigid Body Dynamics
Single rigid body
  The equations of motion are called the “Newton-Euler equations”.
  Well-known acceleration equations
Newton
(translational acceleration)
Euler
(angular acceleration)

## Slide 10: Rigid Body Dynamics
Consider a single rigid body in 2D
  2 translational acceleration equations
  1 rotational acceleration equation
translational
rotational
x
y
xi
θi

## Slide 11: Rigid Body Dynamics
2D Newton-Euler equations in matrix notation
Matrix - vector notation

## Slide 12: Net Force Vector
Forces and torques in the Newton-Euler equations
  Vector fi is the sum of all forces and torques acting on the body.
[ fxi , fyi ]
ti
[ fx1i,fy1i ]
t1i
t2i
Many forces and torques acting on Body i
Net forces and torques acting on Body i
[ fx2i,fy2i ]

## Slide 13: Necessity of Forces
If fi is known, then the dynamics of body i is completely
known.
  It is possible to predict qi, q̇i, and q̈i for all time.
  Note:
    A differential equation solution method is required to get qi, q̇i, and q̈i for all time.
Therefore, the goal is to find fi.
  The difficulty is formulating the forces.

## Slide 14: What is MBD?
What is Multibody Dynamics?
  Dynamics of a system of bodies.
    More than one body.
  The bodies are connected.
    Connected by rigid joints and elastic elements.
Piston
Connecting Rod
Crankshaft
Cylinder/Crankcase
Revolute Joint
(Piston-Connecting Rod)
Revolute Joint
Connecting Rod - Crankshaft
Revolute Joint
(Crankshaft - Crankcase
Translation Joint
(Piston-Cylinder)
Engine System

## Slide 15: Body Connections
Rigid joints
  Examples
    Hinges (Revolute)
    Pistons in cylinders
    Spherical joints
Elastic elements
  Examples
    Springs
    Rubber bushings

## Slide 16: Body Connections
Rigid joints
  Algebraic restrictions on permissible positions
Elastic elements
  Any positions are
  permissible
Good
Bad
Good

## Slide 17: Rigid Joints
Also called constraints or kinematic constraints
An algebraic condition:
  pai = pbj
    These points must always be in the same location
A simplification of reality.
Body i
Body j
pai
pbj
pai = pbj
Body i
Body j

## Slide 18: Rigid Joints
Rigid joints / Constraints are very important.
  Benefit:
    High detail with low computation
    Large time steps
    Reasonable approximation of reality in most cases
  Difficulties
    Difficult to solve equations of motion when constraints exist
    Complex formulation
    Singular configurations
    Possibility of over-constraint

## Slide 19: MBD System of Equations
System equations of motion are written using system matrices and vectors.
Newton-Euler equations of motion for each body
System mass matrix
System acceleration and force vectors
System equations of motion

## Slide 20: System Force Vector f
System force vector f contains all body force vectors fi.
  f is the net forces acting on every body.
    Including connection forces.
      Rigid joint constraint forces
      Elastic forces
    Also gravity and any other forces
Includes all connection forces (constraint, elastic)

## Slide 21: Elastic vs Constraint Connection Formulations
Elastic force and constraint force formulation
  Similar
    But with some key differences
  Elastic forces
    Only depend on body positions
    (and velocities)
  Constraint forces
    Constraint forces are coupled with the body accelerations.
    Constraint forces and accelerations must be found simultaneously.

## Slide 22: Connection Force General Concepts
Connection elements have an element force that acts on points on the bodies.
2 concepts are needed to formulate connection forces
  Expressing the global position of a point on a body
  Transformation of an element force into a body force

## Slide 23: Global Position of a Point on a Body
Connection element forces are applied at a point on a body
The point is defined in the body reference frame.
The point moves with the body.

## Slide 24: Global Position of a Point on a Body
sʹai is the point in the body’s reference frame.
  If the point on Body i is fixed, then sʹai is a constant.

## Slide 25: Global Position of a Point on a Body
sʹai rotates with the body.
sai is the point after rotation.
  Ai is a rotation matrix.

## Slide 26: Global Position of a Point on a Body
Rotation matrix Ai
  v = Aivʹ rotates the vector vʹ counter-clockwise by θi radians around the origin.

## Slide 27: Global Position of a Point on a Body
pai is the global position of sʹai after it is rotated by Ai and translated by Body i’s center of mass xi.

## Slide 28: Derivatives, Vectors, and Matrices
In this document, derivatives of scalars and vectors by vectors are used frequently.
  Derivatives of scalar values:
    The partial derivative ∂s/∂v, where s is a scalar and v is a vector, is the row vector
where

## Slide 29: Derivatives, Vectors, and Matrices
In this document, derivatives of scalars and vectors by vectors are used frequently.
  Derivatives of scalar values:
    The 2nd partial derivative ∂s/∂v∂w of scalar s by vectors v and w is a matrix
where

## Slide 30: Derivatives, Vectors, and Matrices
In this document, derivatives of scalars and vectors by vectors are used frequently.
  Derivatives of vectors:
    The partial derivative ∂v/∂w, where v and w are vectors, is the matrix
where

## Slide 31: Derivatives of Points on Bodies
The derivative of pai with respect to body coordinates qi is required in many parts of the MBD formulation.
Remember:
means: if xi changes, how much does change?

## Slide 32: Derivatives of Points on Bodies
Derivatives of a point on a body w.r.t. the body’s center of mass location
If xi changes, how much does change the same amount.
If yi changes, how much does change the same amount.

## Slide 33: Derivatives of Points on Bodies
Derivatives of a point on a body w.r.t. the body’s rotation angle

## Slide 34: Derivatives of Points on Bodies
The final form of the derivative of pai with respect to body coordinates qi:
Remember:

## Slide 35: Transformation of Element Forces to Body Forces
Every connection has a connection force λ or λe.
The connection force must be transformed into body forces:
  Constraint: fci and fcj
  Elastic: fei and fej.
Element forces
Body forces
Constraint
Elastic

## Slide 36: Transformation of Element Forces to Body Forces
Transformation of an connection element force λ to a body force
  The body force vector for Body i is
    Force components fxi and fyi act on the center of mass.
    Torque ti acts on the body.

## Slide 37: Transformation of Element Forces to Body Forces
If the connection element force is a point force vector λ acting on point sʹai on the body:
Element force
Body force

## Slide 38: Reminder
If we can find f, then we can solve Mq̈ = f.
  And then we know everything.
The goal:
  Formulate the connection forces fc and fe.
Single rigid body
Multiple rigid bodies

## Slide 39: System Force Vector Summation
The system force vector f is the sum of 3 parts:
  Elastic connection forces fe
  Constraint connection forces fc
  Other forces fo
    like gravity and externally applied forces
  fc is going to be converted into fc = −φ,qTλ later.

## Slide 40: Connection Elements
The formulations for elastic and constraint connection element forces are similar.
  The formulations will be shown using 2 examples
    Elastic type:
      Elastic bushing
    Constraint type:
      Revolute joint
Elastic bushing
Revolute constraint

## Slide 41: Elastic Connection Elements
Elastic elements connect 2 (or more) bodies.
Defined by a gap (or displacement) function φ.
  φ can be a scalar or a vector.
    The bushing element’s gap function φ is a vector.
φ2
φ1

## Slide 42: Elastic Connection Elements
Elastic elements generate a restoring force λe when φ ≠ 0.
  The force pushes in a direction that reduces φ.
The simplest and most common force is linear:
  Body i: λei = λe = − kφ
  Body j: λej = −λe = kφ
  Which is λe and which is −λe depends on the formulation of φ.
  The force applied to one body is λe and the other body is −λe.

## Slide 43: Elastic Connection Elements
Note that usually, elastic elements also generate damping forces.
Damping forces are a function of the velocity of the connected points.
We will ignore the damping forces now.
  They are easy to formulate.
Elastic part
Damping part

## Slide 44: Elastic Connection Elements
Elastic element forces λe are a function of body positions only.
Elastic element forces are independent of the acceleration.
So they are computed before acceleration and then summed with the system elastic force vector fe.

## Slide 45: Elastic Connection Elements
There can be many different kinds of elastic elements.
  Examples
    Point-to-point spring
      Non-zero rest length
      1 force component
    Bushing spring
      Zero rest length
      2 force components
    Rotational spring
    Point-on-line spring

## Slide 46: Elastic Connection Element Force Transformation
As previously mentioned, the elastic element force λe must be converted into body forces fei and fej.
  This is the manual method of computing fei.
  There is an automated method that is simpler for a program to execute.
Element force
Body force

## Slide 47: Elastic Connection Element Force Transformation
The elastic element force λe transformation can be transformed automatically using φ,qT.
This will be shown using the elastic bushing element.

## Slide 48: Elastic Element Example: Bushing
Example: a bushing element
  Connects 2 points on 2 bodies
    Point pai on Body i and Point pbj on Body j.
Body i
Body j
Point pai
Point pbj
Bushing element

## Slide 49: Bushing Gap Function
Bushing element gap function
  The gap function φ is a vector.
φ2
φ1
pai
pbj

## Slide 50: Bushing Element Force
Bushing element force
  Simple force: −k times gap
  The element force is also a vector.

## Slide 51: Bushing Element Body Forces
Transformation of elastic element force to body force
  Direct method

## Slide 52: Bushing Body Forces from Derivative of φ
Compare with the derivative φ,qT:

## Slide 53: Bushing Body Forces from Derivative of φ
Compare with the derivative of φ,qT:
The results are the same directly computing the body force vector or using φ,qTλe
Using φ,qT
Using direct computation of fei and fej

## Slide 54: Elastic Body Force From Derivative of φ
The body forces computed directly and computing the using φ,qTλe are the same.
Why?

## Slide 55: Elastic Body Force From Derivative of φ
Answer:
  Same as leverage or mechanical advantage
  Caused by conservation of energy
φ,qT is the mechanical advantage.
  φ,xi, φ,yi, and φ,θi are the change in φ caused by changes in xi, yi, and θi.
  So fxi = φ,xiTλe, fyi = φ,yiTλe, and fθi = φ, θiTλe.
3l
l
fb
fa
ya
yb
so

## Slide 56: Elastic Body Forces in System Acceleration
When computing system accelerations q̈, the elastic forces can be computed first, before evaluating q̈.
  Because the elastic forces only depend on the position coordinates q, they can be evaluated before q̈.

## Slide 57: Elastic Force Complete
The bushing force is now complete.
  The method of computing an elastic force has been completely described.
  It is now possible to calculate
    f = fe + fo
    Mq̈ = f
  If there are no constraints, then q̈ can be computed by factorizing M and back-substituting f.

## Slide 58: Rigid Joint Constraint Forces
Constraints have some similarities to elastic forces:
  They use an identical gap function φ.
  The constraint element force λ is transformed into body forces f by multiplying with the derivative of the gap function φ,qT.

## Slide 59: Rigid Joint Constraint Forces
Constraint forces
  But there are differences with elastic forces:
    A gap is not permitted. This is enforced algebraically:
      φ = 0
    There is no stiffness.
  These cause a few differences in the formulation.
Good
Bad

## Slide 60: Rigid Joint Constraint Forces
gap = 0 is called the constraint equation
  An algebraic equation.
  Strictly enforces the joint condition

## Slide 61: Constraint Force Differences from Elastic Forces
Consider these 2 models
  2 stationary bodies, an external force applied to Body 1.
    Model 1: Bodies connected with a constraint.
    Model 2: Bodies connected with a spring, current at rest (φ = 0).
  Find the values marked “?”.
f 1 = 1N
f 1 = 1N
Body 1
Body 2
Body 1
Body 2
Model 1: Constraint
Model 2: Spring
m2=1kg
m1=1kg
m2=1kg
m1=1kg
λ = ?
φ = 0
λ = ?

## Slide 62: Constraint Force Differences from Elastic Forces
Consider these 2 models
  In Model 1:
f 1 = 1N
f 1 = 1N
Body 1
Body 2
Body 1
Body 2
Model 1: Constraint
Model 2: Spring
m2=1kg
m1=1kg
m2=1kg
m1=1kg
λ = 0.5N
φ = 0
λ = 0N
  In Model 2:

## Slide 63: Constraint Force Differences from Elastic Forces
Consider these 2 models
  In Model 1, the acceleration of the bodies and the constraint force are coupled.
  They are not coupled in Model 2.
f 1 = 1N
f 1 = 1N
Body 1
Body 2
Body 1
Body 2
Model 1: Constraint
Model 2: Spring
m2=1kg
m1=1kg
m2=1kg
m1=1kg
λ = 0.5N
φ = 0
λ = 0N

## Slide 64: Constraint Forces in Acceleration
The acceleration equation for constraints
  The constraint forces and accelerations are dependent.
  They are found simultaneously.
Constrained acceleration equation

## Slide 65: Constraint Example: Revolute Joint
Constraint version of elastic bushing element
  Same gap function as a bushing
    But gap must be zero.
φ1
φ2
Constraint gap function
Gap must be 0

## Slide 66: Constraint: Revolute Joint
Revolute joint element force vector is λ.
  Like the elastic bushing, revolute joint λ is a vector.
    2 components, which matches the gap function.
λ1
−λ1
λ2
−λ2
λ1
λ2
−λ1
−λ2
Constraint forces on each body
Constraint forces

## Slide 67: Constraint: Revolute Joint Body Forces
The revolute joint uses exactly the same formulation as the elastic bushing element for transforming element forces into body forces.

## Slide 68: Another Constraint Example
A translational joint
  Bodies i and j slide on a line relative to each other without rotation
    Like a piston in a cylinder in 2D
  2 constraint equations
    Equation 1: The angular difference between the bodies must be user-defined constant Δ.
    Equation 2: A point on Body j must always be on a specified line on Body i.
nʹi
sʹai
sʹbj
Body i
Body j
where
pbj must always be on the line normal to ni that passes through pai.
Notes: Δ

## Slide 69: Systems of Constraints
Most models have many constraints.
  The slider-crank model has 3 revolute joints and 1 translational constraint.
    Each constraint is composed of 2 constraint equations.
    The whole model has 8 constraint equations.
Body 1
Body 2
Body 3
Cylinder/Crankcase
Revolute
Joint 2
Revolute
Joint 3
Translation Joint
Revolute
Joint 1

## Slide 70: Systems of Constraints
A system of constraint equations is expressed as a single vector of constraint equations:
Body 1
Body 2
Body 3
Cylinder/Crankcase
Revolute
Joint 2
Revolute
Joint 3
Translation Joint
Revolute
Joint 1
Slider-crank example vector φ

## Slide 71: Derivatives of System Constraint Vector
A program that computes derivatives of the constraint vector φ must track which system coordinates each constraint φi is a function of.
  If is a function of body coordinate vectors q j and qk, then
    if m is not j and not k
    The row i of φ will generally have the form
    Therefore, generally, φ,q is a sparse matrix.

## Slide 72: Additional Constraint Equations
The constraint equations add extra variables to the equations of motion:
  In particular, the vector of constraint forces λ.
There are too many unknowns and not enough equations.
  Number of system equations:
    NumBodies * 3
      One equation for every acceleration
  Number of unknowns:
    NumBodies * 3 + NumConstraintEqus.

## Slide 73: Additional Constraint Equations
Additional equations are required to make the system solvable.
There are options for the additional equations.
  Which option is correct depends on the goal.
  Options:
    Constraint equations (without change)
      φ = 0
      This option is often used with implicit differential equation solvers
      This will be discussed tomorrow (Day 2).
    2nd time derivatives of the constraint equations
      dφ/dt2 = 0
      This option is used when computing the accelerations only.

## Slide 74: Additional Constraint Equations for Acceleration
When computing the system accelerations, the additional equations are the 2nd time derivative of the constraint equations.
  The system of equations becomes
  The number of equations becomes are
    NumBodies * 3 + NumConstraintEqus.
  The system of equations is now solvable.

## Slide 75: Gap Function as Function of Time
What is this equation?
  φ = 0 is a set of algebraic restrictions on the values of q.
    Conditions on q that must ALWAYS be true.
  The time derivatives of the restrictions must also be true.
  These time derivatives give us equations governing q̇ and q̈, too.

## Slide 76: Gap Function as Function of Time
Usually, φj is only a function of position coordinates.
Be aware that φj can also be a function of time.
  Example:
    φj = θi − cos(ωt) = 0
  These constraints change with time.
  Usually used to create a driving constraint.
    For example, to make a shaft spin at a given speed to drive other parts of a model.

## Slide 77: Derivatives of Gap Function
It is easiest to express the formulation of d2φi/dt2 for each component of φ independently.

## Slide 78: Derivatives of Gap Function
If φi is only a function of position coordinates
    (not a function of time)
  Then:

## Slide 79: Derivatives of Gap Function
If φi is a function of q and time, then use the chain rule of differentiation to find d2φi/dt2:

## Slide 80: Derivatives of Gap Function
This page is not in the original version of this document. It has been added by a reader for reference.
If =f(q,t)
Then, the total derivative of with respect to the parameter t is
=
If the function is not an explicit function of the parameter t, then , , are equal to zero.

## Slide 81: Derivatives of Gap Function
In both cases,
  where
    If φi is NOT a function of time:
    If φi IS a function of time:

## Slide 82: Derivatives of Gap Function
Solving for the q̈ term:
  produces
In system vector form:
where

## Slide 83: Final Form for Acceleration
Combine the 2nd time derivative of φ with the acceleration equations produces
  In matrix-vector form, this becomes

## Slide 84: Final Form for Acceleration
The form
  is sometimes called “the augmented form” of the equations of motion for MBD.
  This form is well-known in MBD.

## Slide 85: Recursive Formulations
RecurDyn uses a modification of this formulation known as a constrained recursive formulation.
  Recursive formulations reduce the number of unknowns in the equation of motion and many constraint forces.
  A substitution is made in which body coordinates are replaced with rigid joint coordinates.
  The recursive formulation used in RecurDyn is complex and requires a lot of time to explain in detail.
    A simplified version that is much easier to understand is presented here.
    The fundamental concept of the version presented here is very similar to the version used in RecurDyn.

## Slide 86: Recursive Formulations
Most rigid joint constraints have degrees of freedom.
  A revolute joint has 1 joint degree of freedom ψi.
  A joint degree of freedom is relative to the bodies.
  Only fixed joints do not have joint degrees of freedom
    Fixed joints make 2 rigid bodies act like 1 rigid body.
ψi

## Slide 87: Recursive Formulation Degrees of Freedom
The joint degrees of freedom become coordinates of the system.
  In this example, there are 3 joint DOFs.
ψ1
ψ2
ψ3

## Slide 88: Recursive Formulations Body to Joint Relations
The relationship between joint degrees of freedom and body coordinates is computed.
  This changes with the motion of the bodies, so it must be recomputed every time acceleration is needed.
Body coordinates written as function of joint DOFs
Velocity relationship
(linear)
Acceleration relationship (also linear)

## Slide 89: Recursive Formulations
The joint accelerations are substituted for the body accelerations in the equations of motion.
The B matrix is orthogonal to φ,q.
  So φ,qB = 0. Therefore, premultiplying by BT removes the joint constraint forces from the equations of motion.
  Similar to Lagrangian equations of motion, constraint forces aren’t included when using only joint DOFs.

## Slide 90: Recursive Formulations
Only open chains of bodies can be directly formulated.
Closed loops of bodies require a constraint.
  Closed loops must be “cut open” by choosing a constraint to be a “cut joint”.
  This joint remains a constraint in the recursive equations of motion.
Model with a closed loop
Loop opened by “cutting joint”
A “cut joint” remains a constraint
Recursive system degrees of freedom
ψ1
ψ2
ψ3

## Slide 91: Recursive Formulations
For systems with closed loops, some constraints remain in the recursive equations of motion.
  Split φ into and into .
  where
    φr and λr are the recursive joints and constraint forces, which are orthogonal to B.
    φc and λc are the cut joints and constraint forces, which will remain in the equations of motion.

## Slide 92: Recursive Formulations
Then the directly formulated equations of motion become
  Substitution of and pre-multiplication by BT produces
  which simplifies to

## Slide 93: Recursive Formulation Final Equations of Motion
The final form of the constrained recursive formulation equations of motion require additional equations.
  The acceleration formulation becomes:
  or in matrix form:

## Slide 94: Simple Recursive Formulation Example
A simple example of a recursive formulation
  Note that the example formulation here is designed to be easy to understand.
  The recursive formulation used in RecurDyn is more complex.
    RecurDyn’s recursive formulation involves many optimizations that enable it to be computed much faster.
Body 1
Body 2
Body 3
ψ1
ψ2
ψ3
Body 1
Body 2
Body 3
sʹa1
sʹb1
sʹc2
sʹd2
sʹe3
sʹf3

## Slide 95: Simple Recursive Formulation Example
A simple example of a recursive formulation
Body 1
Body 2
Body 3
ψ1
ψ2
ψ3
Body 1
Body 2
Body 3
sʹa1
sʹb1
sʹc2
sʹd2
sʹe3
sʹf3
p0
pb1
pd2
The body position to joint position relationship

## Slide 96: Simple Recursive Formulation Example
The body velocity to joint velocity relationship

## Slide 97: Simple Recursive Formulation Example
Converting the velocity relationship into a matrix-vector multiplication
  Examining the equations of the velocity relationship, it is possible to rewrite them as a series of matrix-vector multiplications.

## Slide 98: Simple Recursive Formulation Example
Continuing the matrix re-arrangement of the velocity equations:

## Slide 99: Recursive Example Velocity Relationship Form
Finally, the velocity relationship can be written as a matrix-vector product
  High performance recursive formulations have much more computationally inexpensive forms of the B matrix.
    But many modifications are required for this.
    For example, all body velocities are expressed in their body reference frames.
Each reduction equation
Combining reduction equations
Final body velocity - joint velocity relationship

## Slide 100: Constraint Complexities
There are some well-known issues with constrained MBD.
  Over-constraint
  Singular configurations
  Solution difficulties
    Much more about this tomorrow

## Slide 101: Constraint Complexities
Constrained MBD issues:
  Over-constraint
    It is possible to have too many constraints.
    Constraints are a mathematical simplification.
    Too many constraints causes the final form of the equations of motion to be singular, so they cannot be solved.
  Singular configurations
    Even if the number of constraints is acceptable, it is possible for a particular position of the bodies to cause the system matrix to become singular.
  Solution difficulties
    The constrained MBD differential equations are not easy to solve.