## Slide 1
Introduction of Math of MBD
2022/04/08
Graham Sanborn
Part 3: Special Features in MBD
Flexible Bodies & Contact
Copyright © 2022 FunctionBay, Inc. All rights reserved.
FunctionBay, Inc. R&D Group.

## Slide 2: Overview
Goal
  Introduce the mathematics of Multibody Dynamics
3 Parts:
  MBD Equations of Motion
  Solving the Equation of Motion
  Special Features
    Flexible bodies
    Contact

## Slide 3: Presentation Parts
MBD requires 2 parts:
  Equations of motion
    f = ma
  The solution to the equations of motion
    time stepping
MBD’s capabilities can be significantly extended with additional features.
  Flexible bodies
  Contact

## Slide 4: Part 3:
Flexible Bodies and Contact

## Slide 5: Flexible Bodies in RecurDyn
Flexible bodies
  There are 2 formulations for flexible bodies in RecurDyn
    FFlex (Full Flex)
    RFlex (Reduced Flex)
  Both are general purpose bodies.
    Can be used in any model for any body.
    Can be connected with constraints or elastic elements to any other body.
    Can make contact with any other body.

## Slide 6: FFlex (Full Flex)
FFlex (Full Flex)
  “Full” means “Full nodal degrees of freedom”.
  Every node is free to move.
  It is a general purpose flexible body.
    Useful for almost every kind of model.
      Complex contact
      Stress concentrations
      Nonlinear deformation (lots of deformation)
      Nonlinear materials (rubber, plastic)
  It is general finite elements
    Modified for MBD
      All elements can rotate.

## Slide 7: RFlex (Reduced Flex)
RFlex (Reduced Flex)
  A flexible body with a very small number of DOFs.
    Uses modal reduction.
      Deformation in vibration mode shapes only
    Simulates VERY quickly.
  Useful for simple flexible problems
    Small deformation only
    Only linear materials
    Deformation similar to vibration mode shapes

## Slide 8: FFlex and RFlex Elements
Both FFlex and RFlex are based on the finite element method (FEM).
  FFlex extends general finite elements (FE) for large rotation.
  RFlex uses FE modal reduction with a rotating reference frame.
So it is important to understand FEM first.

## Slide 9: The Finite Element Method (FEM)
A body is divided into small volumes.
  Each volume is an element.
    Elements have simple shapes.
Original body
Body divided into elements
Simple-shaped elements

## Slide 10: The Finite Element Method (FEM)
The elements can change shape.
  The shapes are controlled by the “nodes”.
Nodes
Moving the nodes changes the shape of the element.

## Slide 11: The Finite Element Method (FEM)
Each element behaves like an elastic spring.
  The spring forces are applied to the nodes.
  Elements make forces to pull the nodes back to their original position.

## Slide 12: The Finite Element Method
The finite element method has 2 main parts
  Nodes: Mass
    Nodal masses become the mass matrix.
  Element: Force
    Element forces become the force vector.
Element forces (and gravity)
Nodal masses

## Slide 13: Common Finite Element Formulation Techniques
The Basis of the finite element method:
  Stresses acting on the face of a tiny cube.
Infinitesimal x forces from stress acting on faces of an infinitesimal cube
Net infinitesimal x, y, and z forces from stress acting on an infinitesimal cube
An infinitesimal cube has stresses on every face.
Notes: σ

## Slide 14: Common Finite Element Formulation Techniques
The finite element formulation can be derived through many methods.
  One common method to derive FEM is virtual work:
  This integral is:
    VirtualDisplacement * (f/vol = m/vol * a)
Gradient (change w.r.t. position) of stress = pressure force/vol
Gravity force density
density * acceleration
Virtual displacement

## Slide 15: Common Finite Element Formulation Techniques
Derivation requires math
  Lots of math.
  There are no simple books.
    Maybe recommend:
      Computational Continuum Mechanics (Shabana, 2008)
A simpler derivation is shown in this document.
  Possible to get basic understanding of FEM without a rigorous derivation.

## Slide 16: Finite Element Mass
Various methods to formulate mass matrix.
  Simplest is lumped mass
    Each node gets a mass like a rigid body
    Fast and easy to compute.
    Reasonably accurate.
  Another method: “Consistent mass”
    Consult a text for information about this formulation.
System mass matrix
Nodal mass matrix
nn = Number of nodes
nnc = Number of nodal coordinates

## Slide 17: MBD Spring Force Formulation
A finite element’s force is like a spring’s force.
  First, recall the MBD spring force formulation from Part 1:
Gap function
Matrix of stiffness coefficients
Multiply by derivative of gap function to transform element force into body forces
Element’s internal force

## Slide 18: Finite Element Force Formulation
A finite element’s force is like a spring’s force.
  The FE elastic force formulation is very similar
    But it uses an integration over the volume of the element.
    (for a linear elastic material)
strain (change of shape) function
Matrix of stiffness coefficients
Multiply by derivative of strain to transform stress into nodal forces
Element’s internal stress

## Slide 19: Spring and Finite Element Force Similarities
MBD and FE forces
  Many of the force formulations are very similar in dynamics.
    Spring elastic forces
    Constraint forces
    Finite element elastic forces
Spring force
Finite element force
Constraint force

## Slide 20: Elastic Energy and Force
The forces are related to energy.
  Spring energy: Spring force:
  FE energy: FE force:
    (for linear elastic materials)

## Slide 21: Energy vs. Energy Density
One difference between spring energy and finite element energy
  The spring formulation uses energy.
  The FE formulation uses energy density.
Energy
Energy density
Spring
Finite Element

## Slide 22: Relation Between Energy and Force
There is a relationship between energy and force
  The force on a coordinate is the derivative of energy w.r.t. that coordinate.
  This can be seen in the definition of work:
    Work is the change in energy.
    Work = force x displacement.
  Therefore, if there is an expression for the strain energy, it can be used to find the nodal forces directly.

## Slide 23: Linear Stress-Strain Relationship
The finite element elastic force for a linear stress-strain relationship is
  where Dε is equal to the stress at a point in the element.

## Slide 24: Linear Stress-Strain Relationship
The stress and strain are expressed in vector form in this equation.
Stress vector
Strain vector
Elastic moduli matrix
(Example: a linear isotropic material)
μ and λ are lame’s parameters.

## Slide 25: Vector Notation
It is possible to derive the finite element force using tensor notation rather than vector notation for the stress and strain.
  Over-bar “ ‾‾ ” means “tensor form”.
    ε̅ is a 2nd order tensor (3x3)
    D̅ is a 4th order tensor (3x3x3x3)
However, in this document, vector notation is used in most cases.

## Slide 26: Strain as Function of Nodal Coordinates
To evaluate the element force, strain is needed.
Strain is a function of nodal coordinates.
  The definition of strain is found in continuum mechanics.

## Slide 27: Strain as Function of Nodal Coordinates
What is ε?
  Strain is function of the derivative of the displacement field w.r.t. position in the field.
    (ε̅l is the small strain formulation)

## Slide 28: The Displacement Field
ε is found from an element’s displacement field.
  An element’s displacement field starts with its nodal coordinates.
q1
q3
q2
The element vector of nodal coordinates
An element, defined by those nodal coordinates

## Slide 29: Element Parameterization
Every element’s volume is parameterized.
  A material point is uniquely identified by a unique set of parameters (ξ1, ξ2, ξ3).
    3D elements usually have 3 parameters.
q1
q3
q2
ξ1 = 1
ξ1 = 3/4
ξ1 = 1/2
ξ1 = 1/4
ξ1 = 0
ξ2 = 1
ξ2 = 3/4
ξ2 = 1/2
ξ2 = 1/4
ξ2 = 0
A 2D triangle element example.
Only has parameters (ξ1, ξ2).

## Slide 30: Position of a Point in an Element
Location of a point r defined by parameters ξ = (ξ1, ξ2, ξ3) is usually a weighted average of the nodal coordinates q1, …, qn.
  The weighting functions are called “shape functions”.
    Shape functions: ni
Weighted average of nodal coordinates
Weighting functions (shape functions)

## Slide 31: Shape Functions
Shape functions ni are a function of only the parameters
ξ = (ξ1, ξ2, ξ3).
  For example, the shape functions for a 2D triangle are:
  Note that
q1
q3
q2
ξ1 = 1
ξ1 = 3/4
ξ1 = 1/2
ξ1 = 1/4
ξ1 = 0
ξ2 = 1
ξ2 = 3/4
ξ2 = 1/2
ξ2 = 1/4
ξ2 = 0

## Slide 32: Example Points in an Element
For example:
  The midpoint of a 2D triangle element.
q1
q3
q2
ξ1 = 1/3
ξ2 = 1/3
r(1/3, 1/3)

## Slide 33: Example Points in an Element
For example:
  A point on the edge between q2 and q3, 25% of the distance from q2 to q3.
q1
q3
q2
ξ1 = 3/4
ξ2 = 1/4
r(3/4, 1/4)

## Slide 34: The Matrix of Shape Functions
The shape functions ni are usually written as a matrix N.
Then the position of a point can be written

## Slide 35: Calculating Deformation
Strain is a measure of deformation.
  To calculate deformation, an undeformed version of the element is required.
Every element has 2 important configurations:
  The current configuration
  An undeformed configuration.
Nodal coordinates of the undeformed configuration.

## Slide 36: Calculating Deformation
The deformation gradient F = dr/dx.
    Draw axis-aligned vectors on the undeformed element.
    The columns of F are the current direction of those vectors.
Undeformed configuration
Current configuration
Axis-aligned lines drawn on the undeformed element.
vʹx = [1 0]T = undeformed x-axis
vʹy = [0 1]T = undeformed y-axis
Current vx = [0.83 0.56]T
Current vy = [1.8 0]T
2D example of the deformation gradient F

## Slide 37: The Mathematics of Deformation
The deformation gradient is fundamental measure of deformation.
  Used to formulate strain.
  Can be easily computed.

## Slide 38: The Mathematics of Deformation
r and x are both functions of ξ.
  So we can calculate the derivatives of r and x w.r.t. ξ.

## Slide 39: The Mathematics of Deformation
For example, N for a 2D triangular element is
So its derivatives w.r.t. ξ1 and ξ2 are
Now r,ξ and x,ξ can be computed.

## Slide 40: The Mathematics of Deformation
Compute dr/dx using the chain rule of differentiation.
dξ/dx is the inverse of dx/dξ.
So:

## Slide 41: Strain
Nonlinear strain is the change in length of an infinitesimal vector on the undeformed body.
  This strain is the “Green-Lagrange strain”.
vʹx = [1 0]T = undeformed x-axis
vʹy = [0 1]T = undeformed y-axis
Current vx = [0.83 0.56]T
Current vy = [1.8 0]T

## Slide 42: Displacement Gradient
Displacement u
  Change in position from undeformed position x to current position r.
x(0, 0) = q01
r(0, 0) = q1
q2 = q02
q3 = q03
x(1/3, 1/3)
r(1/3, 1/3)
u(1/3, 1/3)
u(0, 0)

## Slide 43: Displacement Gradient
The displacement gradient H is related to the deformation gradient F.

## Slide 44: Green-Lagrange Strain using H
Strain using the displacement gradient
  Noting that the conversion from F to H is
  Then the Green-Lagrange strain tensor can be written

## Slide 45: Small Strain
If only considering small displacements, then the nonlinear term HTH is composed of small values squared.
  So the values are so small that they can be ignored.
This produces linear strain:
0

## Slide 46: Small Strain
Small strain can be written in vector form as well.

## Slide 47: Splitting Small Strain
Small strain can be written in the form
  where B is a function of only parameters ξ.
  But to achieve this, derivatives of N w.r.t. x are needed.
  If we have that, the elements of H can be written:

## Slide 48: Splitting Small Strain
N is a function of ξ, not x.
  But we want this.
  We can use this to convert between them
q1
q3
q2
ξ1 = 1
ξ1 = 3/4
ξ1 = 1/2
ξ1 = 1/4
ξ1 = 0
ξ2 = 1
ξ2 = 3/4
ξ2 = 1/2
ξ2 = 1/4
ξ2 = 0

## Slide 49: Splitting Small Strain
Derivatives N,x:
  Shape functions in the undeformed configuration
q01
q03
q02
q01
q03
q02
q01
q03
q02
n1
n2
n3

## Slide 50: Splitting Small Strain
Then use the chain rule of differentiation:

## Slide 51: Splitting Small Strain
The displacement gradient can now be written
If the matrix N is written as rows
then:

## Slide 52: Splitting Small Strain
Then the vector version of small strain can be written:

## Slide 53: Splitting Small Strain
Finally
where

## Slide 54: Derivative of Small Strain
Note that derivatives w.r.t. d (displacement) are equal to derivatives w.r.t. q (nodal coordinates).
  Because
  then
As a result,

## Slide 55: Small Strain Finite Element Force
Small strain element force
  B is constant. It doesn’t change with time. Therefore, the integral can be evaluated before the simulation.
Constant w.r.t. time.

## Slide 56: Constant Stiffness Matrix
Evaluating the integral produces Ke, the element’s stiffness matrix:
  Then the element force is

## Slide 57: Small Strain Finite Element Force
Only small strain elements with linear materials have been presented in the previous slides.
  Accurate for small deformation.
  Inaccurate if the element rotates relative to its reference frame.
  The formulation presented is a very simple, very common formulation.
  Called a “displacement-based” formulation.
    “Displacement-based” means uses continuum mechanics without modification.
    Many modified formulations exist that improve the element accuracy.
RecurDyn also contains large strain elements and nonlinear materials.

## Slide 58: Adapting These Elements for MBD
Bodies in MBD formulations can translate and rotate freely.
  Flexible bodies should be able to translate and rotate, too.
  The common small-strain FE formulation is not capable of simulating element rotation.
  To enable rotation, the formulation must be modified.
The small-strain formulation is usually modified to allow the reference frame to rotate.
  FFlex and RFlex both use translating, rotating reference frames to enable small-strain elements to rotate.

## Slide 59: Adapting These Elements for FFlex and RFlex
FFlex and RFlex both use translating, rotating reference frames.
  FFlex:
    Every element has its own reference frame that moves and rotates with the element.
  RFlex
    A single translating, rotating reference frame is used for all elements in the body.
    Because all elements have the same reference frame, vibration modes can be used to reduce the number of deformation degrees of freedom.

## Slide 60: Full Flex (FFlex)
FFlex is a general-purpose flexible body formulation.
  The nodal coordinates of every element are the DOFs of the body.
    (Unless the nodes are specifically constrained or frozen “boundary condition” elements)
  Every element has its own reference frame to allow it to rotate and translate freely.
  FFlex contains both small strain and large strain elements.
    Only small-strain elements will be discussed here.

## Slide 61: Co-Rotational Formulation
FFlex uses a formulation called a “co-rotational formulation”.
  Every element has its own reference frame.
  An FFlex element’s reference frame is found from its nodal coordinates.
  This allows small-strain, constant stiffness matrices to rotate with the element.
  The calculation of the reference frame is very inexpensive, so this has little affect on computational speed.

## Slide 62: Co-Rotational Reference Frame
Reference frame example:
q1
q3
q2
q1
q3
q2
qʹ1e
qʹ3e
qʹ2e
Nodes at time t
Identify element ref frame
Transform nodes into elem ref frame

## Slide 63: Co-Rotational
To use a co-rotational frame
  First, calculate the reference frame from the nodes.
q3
q2
re
Ae
q1

## Slide 64: Co-Rotational
To use a co-rotational frame
  Next, transform the nodes into element local coordinates
  Calculate displacements
q1
q3
q2
qʹ1e
qʹ3e
qʹ2e
qʹ1e
qʹ3e
qʹ2e
dʹ1e
dʹ3e
dʹ2e
re
Ae

## Slide 65: Co-Rotational
To use a co-rotational frame
  Force is computed relative to the element reference frame
  And it is transformed back to the global coordinates to be added to the system nodal forces.

## Slide 66: Co-Rotational Stress and Strain Recovery
Stress and strain recovery
  Similarly, when computing stresses and strains for user output
    The stresses and strains are calculated in the element reference frame
    Then they are transformed back into global coordinates.

## Slide 67: Reduced Flex
Reduced Flex (RFlex) has 2 main components:
  A single reference frame for all elements in a body that translates and rotates freely.
  Modal reduction
    Deformation is represented using vibration mode shapes.

## Slide 68: RFlex Reference Frame
The body reference frame has 6 DOFs, like a rigid body.
  In 3D:
    3 translational DOFs
    3 rotational DOFs
All deformation is computed from the reference frame.
xi
θi
bi

## Slide 69: RFlex Deformation Representation
RFlex deformation is represented using vibration mode shapes.
  These are the shapes that the body naturally vibrates in.
FE Body
1st vibration mode shape
2nd vibration mode shape

## Slide 70: RFlex Deformation Representation
To use RFlex, the body’s mode shapes must be computed.
  Computed using eigenvalue analysis.
The user chooses how many mode shapes to use.
  Deformation is a sum of these shapes.
  More shapes = more accurate deformation.
  Fewer shapes = faster computation.

## Slide 71: FE Body Matrices
To understand modal reduction, first it is necessary to introduce the FE system matrices.
  A finite element body is composed of multiple elements and nodes.
  Each node has a vector of nodal coordinates qin.
    Nodal coordinates are usually
      the position of the node
      (sometimes) the rotational orientation of the node.

## Slide 72: FE Body Matrices
Flexible system vector of nodal coordinates qf:
  There will be a system vector that contains all of the nodal coordinate vectors for every node in the system.

## Slide 73: FE Body Matrices
Flexible system mass matrix M f:
  The flexible system has a single system mass matrix that contains all of the masses of all nodes.
    RecurDyn uses “lumped masses”, in which each node has a mass similar to a rigid body.
    Every node’s mass is a sum of the mass contributed to it by every element it is attached to.
System mass matrix
Nodal mass matrix
nnc x nnc (number of nodal coordinates) matrix
Off diagonal terms can be non-zero.
nn x nn (number of nodes) matrix of sub-matrices
Lumped mass matrix, so off-diagonal sub-matrices are 0.

## Slide 74: FE Body Stiffness Matrix
The flexible system stiffness matrix
  For small strain elements that:
    Have constant stiffness matrices
    All elements share the same reference frame.
  Then there is a system stiffness matrix K f .
    It has a sub-matrix ki,jn for every pair of nodes i and j.
Stiffness coefficients that connect nodes 1 and 2 in the system
System stiffness matrix

## Slide 75: Element Stiffness Sub-Matrices
Every small-strain element with index k has an element stiffness matrix .
  contains sub-matrices of stiffness coefficients that connect 2 nodes.
Stiffness coefficients that connect nodes 2 and 3
Element stiffness matrix

## Slide 76: FE Body Stiffness Matrix
The flexible system stiffness matrix
  Each sub-matrix ki,jn is the sub-matrix of stiffness coefficients associated with nodes i and j.
Σ
System sub-matrix 2,3 is sum of element 1’s (2,3) and elements 2’s (2,3) sub-matrices.
Element 1’s stiffness
Element 2’s stiffness
No elements connect nodes 1 and 4.
System stiffness
q1
q3
q2
q4
Element 1
Element 2

## Slide 77: FE Modal Reduction
To understand RFlex, first, modal reduction must be understood.
Modal analysis is performed on the system mass and stiffness matrices of a finite element body.
  Relative to the body’s reference frame.
  This requires that the elements are small deformation elements so that they have constant stiffness matrices.

## Slide 78: FE Modal Reduction
The equations of motion of linear (small deformation) FE body is given by
  (Ignoring damping)
Modal analysis is performed on the unforced system equations:

## Slide 79: FE Modal Reduction Mode Shapes
Main assumption:
  The body vibrates in harmonic motion in specified shapes.
  In other words, vibration in any shape is specified by a mode shape vector ψi and a magnitude of vibration bi.

## Slide 80: FE Modal Reduction Mode Shapes
Main assumption:
  The body vibrates in harmonic motion in specified shapes.
  In other words, vibration in any shape is specified by a mode shape vector ψi and a magnitude of vibration bi.
bi = 1
bi = 4

## Slide 81: FE Modal Reduction Mode Shapes
The total deformation shape during vibration is the sum of all vibration modes simultaneously:

## Slide 82: Vibration Mode Dynamics
For any mode of vibration defined by mode shape vector ψi and a magnitude of vibration bi, the equations of motion for that mode are

## Slide 83: FE Vibration Similarity to 1 DOF Oscillator
The body equations of motion are now similar to a 1 DOF oscillator
  It must be that every row of the system of equations is scalar of the same equation:

## Slide 84: Vibration: The Eigenvalue Problem
Substituting the known solution into the modal equations of motion produces
  which simplifies to

## Slide 85: Vibration: The Eigenvalue Problem
This equation must be true always
  including when t ≠ 0.
  This can only be true if the coefficient is 0.

## Slide 86: Vibration: The Eigenvalue Problem
This is the classical eigenvalue problem.
  The eigenvalue problem
where

## Slide 87: Vibration: The Eigenvalue Problem
This is an eigenvalue problem for matrix A.
  ψi is any eigenvector of A.
  λi is its associated eigenvalue.
A represents wave dynamics of the mass and stiffness of the system.
  ψi is will be a shape in which the body naturally vibrates at a given frequency of ωi = (λi)1/2.

## Slide 88: Equivalent 1 DOF Oscillating System
Substituting one of these eigenvectors back into the original equations of motion of the body produces
  in which every row is the same equation, differing by the force term and a scalar value.

## Slide 89: Equivalent 1 DOF Oscillating System
The equivalent 1 DOF model needs to account for every force acting on every node.
  The equivalent 1 DOF force is a weighted sum of the force elements.
  The weighting is the mode shape itself.
  The 1 DOF system can be found by pre-multiplying by the transpose of ψi.
  which reduces to

## Slide 90: A System of Modes
However, if the FE body has n DOFs, then there are n eigenvalues and eigenvectors.
  Ψ is a square matrix.

## Slide 91: A-Orthogonality of Mode Shapes
The eigenvectors are orthogonal to each other.
  Specifically, they are A-orthogonal to both M and K.
    If i ≠ j, then

## Slide 92: System Equations of Motion
Pre-multiplying the equation by ΨT produces an identical n DOF system
  Because of A-orthongality, Mψ and Kψ are diagonal.
  The dynamics of the FE body has not changed.
  But each DOF is independent of all others.

## Slide 93: Reducing the DOFs
Usually, we don’t use all of the mode shapes.
  We choose only a subset of them.
    A small subset.
    The lowest frequency modes only.
    We choose how many we want to use (say, m mode shapes).
      where m « n.
    Ψm is generally not square. Usually, it has very few columns
    (compared to Ψ)

## Slide 94: The Reduced System with m DOFs
Using the reduced Ψm and Λm produces
  which becomes
  In this system, Mc and Kc are m x m diagonal matrices, and there are only m DOFs in bc.
  All DOFs are all totally independent of each other.

## Slide 95: Modal Reduced System
The reduced FE system usually has very few degrees of freedom.
  The accuracy of the dynamics of these equations depend on the load conditions.
    It is accurate if the true deformation is similar to the chosen vibration mode shapes.
    If the true deformation should be different than a sum of the chosen mode shapes, then the accuracy is low.

## Slide 96: RFlex: Modal Reduction and a Reference Frame
RFlex requires a body reference frame that moves and rotates.
  The global position of any point on a body is given by:
    (This is the same equation used in the MBD formulation)
The point in the body reference frame
The reference frame rotation matrix
The origin of the reference frame in the global system

## Slide 97: RFlex: Modal Reduction and a Reference Frame
An RFlex body deforms.
  So sʹ moves relative to the reference frame.
The local point is not constant.

## Slide 98: RFlex from a Modal Reduced FE Body
Modifying the global position equation for a flexible body that uses modal reduction:
The global position of a local, modal reduced point
The global position of a local point
The local point moves relative to the reference frame
Displacement relative to the body reference frame specified with modal reduction
Undeformed nodal coordinates relative to the body reference frame

## Slide 99: RFlex from a Modal Reduced FE Body
Position on an RFlex Body
x
θ
bc
Ψc

## Slide 100: RFlex Derivation
The equations of motion for an RFlex body must be derived from a proper source.
  The key difference between finite element formulations is the expression for r.
Gradient (change w.r.t. position) of stress = pressure force/vol
Gravity force density
density * acceleration
Virtual displacement

## Slide 101: RFlex Equations of Motion
After all terms are computed, the RFlex equations of motion for a single body look like:
  and Qd is a vector of mass and velocity components commonly referred to as the “quadratic velocity terms”
    For example
      Coriolis terms
      Gyroscopic force terms

## Slide 102: MFBD = MBD + FFlex + RFlex
RecurDyn’s DAEs combine all 3 body types into 1 system of equations.
The system equations of motion:
  All matrices and vectors include parts for
    Rigid bodies
    Full Flex bodies
    Reduced Flex bodies

## Slide 103: System Equations of Motion
The system equations of motion:
  Each matrix and vector contains sub-matrices and sub-vectors of parts for rigid, RFlex, and FFlex bodies.
  Superscript meaning:
    r : rigid
    d : reduced flex (RFlex)
    f : full flex (FFlex)

## Slide 104: System Equations of Motion
Constraints:
  Constraints can be defined between any body types.
  For example, a constraint φi can constrain a rigid body to an FFlex node.
    Any combination of body types is possible in a constraint.
RFlex matrices and FFlex forces are contained in the elastic force vector fe.
  There is no system FFlex stiffness matrix.
  Each FFlex element is evaluated independently.
Contains connection forces and constraints for any body to any other body

## Slide 105: Solving the System Equations of Motion
RecurDyn solves the entire system of DAEs together with a single numerical DAE solver.
  A single time step is used for all equations of motion.
  The DAEs are solved as a “monolithic system”.
    It is not “co-simulation”, which uses different solvers for different parts.
(The equations shown here are the Newmark method)

## Slide 106: FFlex RBE (FDR) and RBE3
Connections to FFlex bodies
  Should not attach constraints or elastic elements to a single node of an FFlex body.
    This creates very unrealistic deformation in the body.
  Should distribute connection forces over a large region of the mesh.
The force of a connection here should be distributed over many nodes

## Slide 107: FFlex RBE (FDR) and RBE3
Connections to FFlex bodies
  This is done with “Rigid Body Elements” (RBE).
  There are 2 kinds of RBE elements in RecurDyn.
    RBE “Rigid Body Element” elements
      (also called FDR “Force Distributing Rigid”) elements
    RBE3 elements
      (also called Interpolation) elements.

## Slide 108: RBE Elements
RBE elements are like RBE2 elements in NASTRAN
  Truly a rigid element.
  Constrains a group nodes together.
    Their relative positions are completely constrained.
    Constrains position and rotation of nodes.

## Slide 109: RBE Elements
RBE elements are like RBE2 elements in NASTRAN
  The constrained nodes act like a rigid body.
  The part of the mesh that is constrained by an RBE element cannot deform.
    This part of the mesh becomes rigid.
  Note: A constraint version and a stiff elastic version are implemented in RecurDyn.
The nodes constrained with an RBE element move like a rigid body

## Slide 110: RBE3 Element
RBE3 elements are like RBE3 elements in NASTRAN.
  A non-rigid, force-distributing element.
  A constraint.
    There is no elastic option for this element.
  2 parts in the RBE3 constraint.
    Position (translation)
    Rotation
  The RBE3 element allows the slave nodes to move.
    The RBE3 element will not make a part of the mesh rigid.

## Slide 111: RBE3 Element
RBE3 elements are like RBE3 elements in NASTRAN.
  Be aware:
    The RBE3 element cannot be used in all cases.
      The slave nodes cannot be co-linear.
      It is best if the master node is not close to any slave nodes.
    RBE ≠ RBE3.

## Slide 112: RBE3 Element
Position constraint
  There is a master node and a set of slave nodes.
  The master node is constrained to be in the average location of the slave nodes.

## Slide 113: RBE3 Element
Rotation constraint
  The orientation of the master node is constrained to the position of the slave nodes.
    The orientation of the master node is the orientation that minimizes the angular differences between the current directions to the slave nodes.
      Minimizes the squares of the angles.
RBE3 Original Config.
RBE3 Original Config.
Blue lines are the directions to the nodes in the initial configuration
Current orientation of master node minimizes the angular differences to the slave nodes.
θφ4
θφ1
θφ3
θφ2

## Slide 114: Contact
In MBD, “Contact” is an algorithm that calculates forces caused by bodies touching each other.
  It prevents interpenetration of bodies.
  It creates friction forces and slipping forces.
RecurDyn uses a penalty-based contact formulation.
  Penetration between the bodies is permitted.
    The normal force of contact is proportional to the amount of penetration.
  Contact between any 2 bodies is permitted.
    Rigid
    FFlex
    RFlex
  The algorithm is mostly the same for all 3 body types.
  There are various contact algorithms implemented in RecruDyn.
    Only GeoContact is discussed in this document.

## Slide 115: Contact Detection
Contact is detected by processing mesh geometry.
  Bodies are meshed.
    Polygons, Vertices
  Detection:
    Find vertices of one body passing through the mesh polygons of the other.
    Any vertex that is inside of the other mesh is considered to be in contact.
  Contact location
    For any vertex inside the other mesh, a point on the mesh is found as the matching point of contact on the mesh.
    The line from the vertex to the surface must be perpendicular to the surface of the mesh.
Every vertex can make contact independently.
  If more than 1 vertex has passed through the other mesh, then each vertex is treated as a point of contact.
2 bodies
Contact detected between the bodies
Red lines are penetration lines to closest points on polygons.

## Slide 116: Contact Normal Force
The contact normal force is implemented as a spring.
  The contact normal force is proportional to the penetration.
    (this above formula does not include damping)
User-definable exponent (default is 1)
Penetration
User-definable contact stiffness

## Slide 117: Step Size and Contact
Accuracy depends on solver time step size.
  For a contact to produce accurate results:
    Start of contact:
      It must be detected soon after penetration begins.
    End of contact
      It must only exit a small amount in the time step that contact ends.
time = ti
time = ti+1
time = ti
time = ti+1

## Slide 118: Step Size and Contact
At the start of the time step:
  If there is no penetration, no contact force is used.
No contact at start of time step.
Contact not used during this time
time = ti
Contact exists at start of time step.
Contact is used during this time
time = ti

## Slide 119: Step Size and Contact
At the start of the time step:
  At the start of new contact
    If the vertex penetrates deeply before the beginning of the first detection, a huge normal force is calculated.
    This force adds energy to the system.
    It can add a huge amount of energy.
The node penetrates too deeply. The penetration is deeper than the expected maximum penetration for this contact. The normal contact reaction force will be too large.
time = ti-1
time = ti
Expected maximum penetration

## Slide 120: Step Size and Contact
At the start of the time step:
  At the end of an existing contact
    If the vertex escapes the surface a large distance during its last step of contact, the spring will remove energy from the bodies.
    It will apply an unrealistic cohesive force, pulling the bodies back together.
The node starts the time step in contact, so contact is used during this step. The node travels far out of the mesh during the step. An unrealistic amount of energy will be lost because the contact was applied too long.
time = ti+1
time = ti
Between ti and ti+1, the contact force will unrealistically pull the node down (like a cohesion force)

## Slide 121: Step Size and Contact
Solution: Use small time steps when contact is about to begin or end.
  This will minimize:
    The penetration before the first time step that contact is detected.
    The separation of the vertex from the mesh on the last time step of contact.
  Bounding boxes:
    RecurDyn has an option to detect when contact surfaces are close. When they are close, the solver can reduce the maximum time step by a fixed factor.
Bounding boxes around the contact surfaces
When the bounding boxes intersect, the maximum time step is reduced by fixed factor to improve contact response.

## Slide 122: Thank You