## Slide 1
Introduction of Math of MBD
2022/04/07
Graham Sanborn
Part 2: Solving the MBD Equations of Motion
Copyright © 2022 FunctionBay, Inc. All rights reserved.
FunctionBay, Inc. R&D Group.

## Slide 2: Overview
Goal
  Introduce the mathematics of Multibody Dynamics
3 Parts:
  MBD Equations of Motion
  Solving the Equation of Motion
  Special Features
    Contact
    Flexible bodies

## Slide 3: Presentation Parts
MBD requires 2 parts:
  Equations of motion
    f = ma
  The solution to the equations of motion
    time stepping
The third part extends MBD’s capabilities.
  Flexible bodies and contact

## Slide 4: Part 2:
Solving the MBD equations of motion

## Slide 5: MBD Equations of Motion
The MBD equations of motion are the acceleration equations.
Solving these equations produces q̈ and λ.
  From the values of q and q̇.

## Slide 6: Solving the Differential Equation
Getting q, q̇, q̈, and λ from time t = 0 to time t = tend is called “solving the equations of motion”.
  Really, this is solving a differential equation (DE).
t
t0
t1
t2
t3
t4
t5
tend

## Slide 7: What is a differential equation (DE)?
An equation that defines a relationship between a function and its derivatives.
  A 1st order DE might look like this:
  y is a function.
    It is unknown.
    A function of x.
      y = a(x)
  yʹ is dy/dx.
    The DE yʹ = g(x,y) is 1st order
      It only contains the first derivative of y.

## Slide 8: Forms of DEs
Some DEs cannot be written:
The most general form of a 1st order DE is
  Here, yʹ cannot be separated out of g.
This document mostly uses yʹ = g(x,y).
  But both versions could be used anywhere in this document.

## Slide 9: DEs as Systems of Equations
DEs are often a system of equations.
  In this case,
  or
  y, yʹ, and g are vector quantities.
  The methods of solving scalar DEs and vector DEs are mostly identical.

## Slide 10: Understanding a 1st order DE
Every point on the x-y plane has a slope.
Example 1st order DE:
x
y
yʹ at (1,1)

## Slide 11: Understanding a 1st order DE
1st order DE example
  Solutions:
    There are infinitely many solutions.
    For a given x0, every y0 produces a different solution.
Some example solutions
Points with same x0 = −1
x
y

## Slide 12: Understanding a 1st order DE
1st order DE example solutions:
  Solution: y = a(x).
  Each y is a function.
    It has 1 value at any x.
5 example solutions
Solution containing (-1,-0.5)

## Slide 13: 2nd order DEs
A 2nd order DE relates a function y and its 1st and 2nd derivatives yʹ and yʺ:
  or
  where

## Slide 14: Newton-Euler Equations as DEs
The Newton-Euler equations are 2nd order DEs:
The independent variable is t and the unknown vector of functions is q.
  The solution is

## Slide 15: MBD Equations of Motion are Special DEs
Usually, “The MBD equations of motion” means the equations of acceleration. For MBD, these are:
But the equations used to solve the DEs can be different.
  This will be shown in much more detail later.
Not the derivative of φ.
This is φ̈

## Slide 16: Solving a DE
Usually, “solving the DE” means finding the functions
  y = a(x)
  yʹ = aʹ(x)
  over some interval of x.

## Slide 17: No Analytical Solutions
Most DEs have no analytical solution.
  No expression for a(x) or aʹ(x) is known to exists.
  The DEs for MBD have no analytical solution.

## Slide 18: Numerical Methods to Solve DEs
Numerical methods are used to find approximate DE solutions.
  “Solving the DE numerically” means finding approximate points in the solution:
    (xi,yi) and (xi,yʹi) for i = 0 to nend
x0
x1
x2
x3
x4
x
y
(x0, y0)
(x1, y1)
(x2, y2)
(x3, y3)
(x4, y4)

## Slide 19: Euler’s Method
Most basic numerical method for solving a DE:
  Euler’s method
    Approximate y = a(x) as a series of points.
      (xi,yi)
    Each point yi+1 is calculated from the previous point yi at xi using the slope dy/dx calculated at (xi,yi).
x0
x1
x2
x3
x4
x
y
(x0, y0)
(x1, y1)
(x2, y2)
(x3, y3)
(x4, y4)

## Slide 20: Euler’s Method
Given a known point in the solution:
  (xi,yi)
then dy/dx at (xi,yi) can be computed directly from g.
x
y

## Slide 21: Euler’s Method
Assume that dy/dx is constant between xi and xi+1.
Then step to (xi+1, yi+1) using
x
y

## Slide 22: Euler’s Method
Again, approximate the step to the next point using the same algorithm from (xi+1, yi+1) to (xi+2, yi+2).
x
y

## Slide 23: Numerical Solution Error
Error in numerical approximation
  There is error in every numerical method for solving DEs.
    The error is unavoidable.
    However, the error can be reduced though various methods.
  Euler’s method will not exactly match the true solution.
    The difference between the true solution and Euler’s method is error.
Error
True solution
Euler’s method
x
y

## Slide 24: Euler’s Method Error
Source of error in Euler’s method’s
  The true solution’s slope is not constant between xi and xi+1.
  Euler’s method assumed that it was constant.
True solution
Euler’s method
x
y
Error
(difference between true and approximated solution)

## Slide 25: Euler’s Method Error
Euler’s method error reduction:
  A smaller step size usually creates less error.
Error decreases for smaller step sizes
Possible values for
x
y

## Slide 26: Error Reduction
Be aware:
  Smaller steps don’t always create smaller error.
Error increases with a slightly smaller step size
x
y
Possible values for

## Slide 27: Euler’s Method Example
Euler’s method 1st order error example:
  Using the previous 1st order DE example
    Solution containing (x,y) = (−1, 0.6)
True solution
x
y

## Slide 28: Euler’s Method Example
Euler’s method 1st order error example:
  Using Euler’s method to find an approximate solution
    h = 1/2
x
y

## Slide 29: Euler’s Method Example
Euler’s method 1st order error example:
  Using Euler’s method to find an approximate solution
    h = 1/4
x
y

## Slide 30: Euler’s Method Example
Euler’s method 1st order error example:
  Using Euler’s method to find an approximate solution
    h = 1/8
x
y

## Slide 31: Euler’s Method Example
Euler’s method 1st order error example:
  Using Euler’s method to find an approximate solution
    h = 1/16
x
y

## Slide 32: Euler’s Method Example
Euler’s method 1st order error example:
  Using Euler’s method to find an approximate solution
    h = 1/32
x
y

## Slide 33: Euler’s Method Example
Euler’s method 1st order error example:
  Using Euler’s method to find an approximate solution
    h = 1/64
x
y

## Slide 34: Euler’s Method on the Circular DE
Euler’s method on 1st order DE circle example:
  A system of DEs.
  This DE has a simple analytical solution:

## Slide 35: Euler’s Method on the Circular DE
Euler’s method on 1st order DE circle example:
  It forms circles of any radius, centered at the origin (0,0).
One true solution and y’
y1
y2

## Slide 36: Euler’s Method on the Circular DE
Euler’s method on the circle DE
  Each step i is in the direction of yʹi.
  Each step moves away from (0,0).
  Euler’s method is unstable.
    The Euler solution will go to infinity.
y1
y2

## Slide 37: Euler’s Method Summary for 1st Order DEs
Euler’s method is very simple, very easy to understand.
  Maybe the most obvious and simple method.
y moves from yi to yi+1 in direction yʹi.
Euler’s method’s error is significant.
  The error grows unstably.
    Will eventually go to infinity in many problems.
  Reducing step size usually decreases solution error.

## Slide 38: Euler’s Method with 2nd Order DEs
MBD and dynamics is not 1st order.
  It’s 2nd order.
  Euler’s method can be used with 2nd order DEs, too.
  With Euler’s method, the usual method is to use Euler’s method on each variable.

## Slide 39: Euler’s Method with 2nd Order DEs
Euler’s method can be used with 2nd order DEs, too.
  Use Euler’s method twice
    For y
      The derivative of y is yʹ.
    For y’.
      The derivative of yʹ is g.
yʹ is one of the solution functions.

## Slide 40: Euler’s Method with 2nd Order DEs
Same as 1st order Euler’s method, but used twice.
  Once for y and once for yʹ, every step.
The derivative of y is y’, which is already known at xi.
The derivative of y’ is found from g().
Position stepping
Velocity stepping
x
y
x
yʹ

## Slide 41: Euler’s method for 2nd order DEs
Similarly to the 1st order Euler’s method, the process is repeated for each additional step.
Position stepping
Velocity stepping
x
y
x
yʹ

## Slide 42: 1 DOF Oscillator Example: Euler’s Method
2nd order Euler’s method example:
  1 DOF oscillator, no damping
    mass m
    stiffness k
    displacement y
y
m
k

## Slide 43: 1 DOF Oscillator Equations of Motion
The equation of motion is
A simple 1DOF oscillator preserves energy.
  Energy = kinetic energy + elastic strain energy
  Should not change over time.
  Energy is the easiest to use method of evaluating the accuracy of the DE solution method on this problem.

## Slide 44: 1 DOF Oscillator True Solution
A well-known closed form solution exists for this model. It can be used to verify the accuracy.
  Assuming initial conditions
  Known solution is:

## Slide 45: 1 DOF Oscillator True Solution
1 DOF oscillator true solution
t
y0 = 0
ẏ0 = 1
k = 10
m = 1
ω = 3.162
a = 0.3162
p = 1.987
U = 0.5
a = max amplitude
p = period
U = total energy
y
ẏ
U

## Slide 46: 1 DOF Oscillator Example: Euler’s Method
Euler’s method with the 1 DOF oscillator
  h = 1/4
y
ẏ
U
The time step is too large.
Very unstable.
Error grows very rapidly.
The solution goes to infinity very quickly.
Energy rises extremely fast.

## Slide 47
Euler’s method with the 1 DOF oscillator
  h = 1/16
The time step is too large.
But now the correct trend of the solution can be seen.
y
ẏ
U

## Slide 48
Euler’s method with the 1 DOF oscillator
  h = 1/64
The time step is large.
But now the correct trend of the solution can be seen.
y
ẏ
U

## Slide 49
Euler’s method with the 1 DOF oscillator
  h = 1/256
The solution is almost useful.
Energy only rises a little during the simulation.
y
ẏ
U

## Slide 50
Euler’s method with the 1 DOF oscillator
  h = 1/1024
Now the solution is mostly acceptable.
If the oscillator had material damping, the solution might be reasonable.
y
ẏ
U

## Slide 51: Euler’s Method Summary
Simplest numerical method to solve DEs.
When used with Newton-Euler equations, energy grows.
  Not stable
  If the true solution is stable, then the Euler’s method solution will diverge.
  If the true solution has damping, then Euler’s method might be reasonable if the time step is small enough.
  Accuracy can be increased by reducing time step size.
    But the error just grows more slowly.

## Slide 52: Euler’s Method Summary
Euler’s method with the 1 DOF oscillator
  h = 1/1024
  for 200 sec.
y
ẏ
U
Even with the smallest time step, the solution goes to infinity.
The solution is only reasonable if the simulation is short.

## Slide 53: Symplectic Euler’s Method
There are other, better numerical methods for solving DEs for dynamics.
  For example, a small change to Euler’s method for 2nd order DEs:
    Creates the “symplectic Euler’s method”.
    Also called the “semi-implicit Euler’s method”.
Euler’s method
Symplectic Euler’s method
Initial velocity used to step position
Final velocity used to step position

## Slide 54: Symplectic Euler’s Method
Comparison of Euler’s method to the symplectic Euler’s Method:
y
ẏ
y
ẏ
Euler’s method
Symplectic Euler’s method
Position’s slope is velocity at ti
Position’s slope is velocity at ti+1
x
x
x
x

## Slide 55: Symplectic Euler’s Method
With the symplectic Euler’s method, velocity step is computed before position.
  Because updated velocity is needed to compute position step.
y
ẏ
Position’s slope is velocity at ti+1
Compute velocity first.
Compute position second.
x
x

## Slide 56: Symplectic Euler’s Method on 1 DOF Oscillator
1 DOF oscillator example using the symplectic Euler method
  h = 1/4
y
ẏ
U
The energy is not constant, but it oscillates stably around a specific value.
Though the solution accuracy is low, it has mostly the correct shape.
There is a small phase shift from the true solution.

## Slide 57: Symplectic Euler’s Method on 1 DOF Oscillator
1 DOF oscillator example using the symplectic Euler method
  h = 1/16
y
ẏ
U
The solution is now reasonable.
There is a small phase shift in the velocity.
The energy is within 10% of the true energy at all times.

## Slide 58: Symplectic Euler’s Method on 1 DOF Oscillator
1 DOF oscillator example using the symplectic Euler method
  h = 1/64
y
ẏ
U
The solution is good.

## Slide 59: Symplectic Euler’s Method on 1 DOF Oscillator
1 DOF oscillator example using the symplectic Euler method
  h = 1/256
y
ẏ
U
The solution is now very good.
Energy is within 1% of true energy.

## Slide 60: Symplectic Euler’s Method on 1 DOF Oscillator
1 DOF oscillator example using the symplectic Euler method
  h = 1/1024
y
ẏ
U
The solution is excellent.
The energy is within 0.2% of the true energy.

## Slide 61: Symplectic Euler’s Method Summary
The symplectic Euler’s method preserves energy with the 1 DOF oscillator.
  If h < 2/ω, and if h is constant, then the solution is stable.
  The position and velocity don’t go to infinity.
  The energy oscillates stably around a fixed value.
    Total energy, h = 1/4, for 200sec.
U

## Slide 62: Symplectic Euler’s Method Stability
The symplectic Euler’s method has stability limits.
  If the time step is too large (h < 2/ω), then the solution becomes unstable.
y
ẏ
U

## Slide 63: Symplectic Euler’s Method Limits
Symplectic Euler are not useful for stiff DEs.
  A “stiff” DE has some high frequency oscillations.
    It is stiff even if the high frequency DOF is unimportant or the amplitude is extremely small.
  The solution is only stable if h < 2/ωmax.
    ωmax is the highest oscillating frequency in the system.
    Ideally, h should be much smaller than 2/ωmax.
Many MBD systems have very stiff springs.
  Bushing elements
  Contact stiffness

## Slide 64: Implicit Backward Euler’s Method
For MBD, a better numerical DE solution method would be able to take much larger steps stably.
There are numerical methods to solve DEs that are guaranteed to be stable regardless of step size and stiffness.

## Slide 65: Implicit Backward Euler’s Method
One such method is the implicit backwards Euler’s method.
  For 1st order DEs, the method is
  The different from standard Euler’s method is small.
    The standard Euler’s method is
  This method is called “implicit” because yʹi+1 depends on the unknown value yi+1.
yʹi+1 depends on yi+1
doesn’t depend on yi+1

## Slide 66: Implicit Backward Euler’s Method
Meaning of the backward implicit Euler’s method:
  (Remember, xi+1 is a given value.)
Find a point at this x whose slope passes through the initial point
xi+1
xi
(xi, yi)

## Slide 67: Implicit Backward Euler’s Method
Meaning of the backward implicit Euler’s method:
  (Remember, xi+1 is a given value.)
The slope from this point must pass through the initial (xi, yi) point.
We must find yi+1 that satisfies this property.
xi+1
xi
(xi, yi)
(xi+1, yi+1)
yʹi+1

## Slide 68: Solving an Implicit Backward Euler Step
Solving the backward implicit Euler method requires solving these equations:
  If g(xi+1, yi+1) is nonlinear, then a nonlinear equation solver is needed.
    For example, Newton’s method.

## Slide 69: Solving an Implicit Backward Euler Step
Solving the backward implicit Euler method using Newton’s method:
  Use the first equation to write yʹi+1 as a function of yi+1.
  Then convert the second equation into the Newton residual r:

## Slide 70: Solving an Implicit Backward Euler Step
Solving the backward implicit Euler method using Newton’s method:
  Then find yi+1 such that r(yi+1) = 0.
  First, set yi+1 to an initial guess.
    For example, yi+10 = yi
    where the superscript 0 indicates the iteration count.

## Slide 71: Solving an Implicit Backward Euler Step
Solving the backward implicit Euler method using Newton’s method:
  Iterate using
  until |r j| < ε
    (ε is a user-defined small tolerance)

## Slide 72: Circle DE with the Implicit Backward Euler’s Method
Solving the circle DE using the implicit backward Euler method
  Every step moves closer to the origin.
    The error in each step adds stability to the solution.
  The accuracy is similar to the explicit Euler method.
  The solution is very stable.
    It does not go to infinity.

## Slide 73: Implicit Backward Euler with 2nd Order DEs
Identically with the standard Euler’s method, the implicit backward Euler’s method can solve 2nd order DEs.
  For 2nd order DEs, the method is applied twice
    Once for position
    Once for velocity.

## Slide 74: Implicit Backward Euler with 2nd Order DEs
Solving a time step of 2nd order DE backward Euler
  The method is described by 3 equations:
  The first 2 equations are used to write ẏi+1 and ÿi+1 as functions of yi+1.

## Slide 75: Implicit Backward Euler with 2nd Order DEs
Solving a time step of 2nd order DE backward Euler
  The equation that defines ÿi+1 is converted into a Newton residual:
  To solve r(yi+1) = 0, use Newton’s method.
    This requires the derivative:
where

## Slide 76: Implicit Backward Euler with 2nd Order DEs
Solving a time step of 2nd order DE backward Euler
  Solve r(yi+1) = 0 iteratively
    until |r j| < ε

## Slide 77: Implicit Backward Euler with the 1 DOF Oscillator
Solving the 1 DOF oscillator 2nd order DE using the implicit backward Euler method
  h = 1
y
ẏ
U
The time step is very large, but the solution is completely stable.
Accuracy is very low.
The energy disappears extremely quickly.

## Slide 78: Implicit Backward Euler with the 1 DOF Oscillator
Solving the 1 DOF oscillator 2nd order DE using the implicit backward Euler method
  h = 1/4
y
ẏ
U
The accuracy is still very poor.
The energy is still disappears very quickly.

## Slide 79: Implicit Backward Euler with the 1 DOF Oscillator
Solving the 1 DOF oscillator 2nd order DE using the implicit backward Euler method
  h = 1/16
y
ẏ
U
The solution is beginning to follow the curve.

## Slide 80: Implicit Backward Euler with the 1 DOF Oscillator
Solving the 1 DOF oscillator 2nd order DE using the implicit backward Euler method
  h = 1/64
y
ẏ
U
The solution follows the curve enough to see the gross behavior.
The energy drops quickly.

## Slide 81: Implicit Backward Euler with the 1 DOF Oscillator
Solving the 1 DOF oscillator 2nd order DE using the implicit backward Euler method
  h = 1/256
y
ẏ
U
The solution is becoming good.
The energy drops slowly.

## Slide 82: Implicit Backward Euler with the 1 DOF Oscillator
Solving the 1 DOF oscillator 2nd order DE using the implicit backward Euler method
  h = 1/1024
y
ẏ
U
The solution is excellent.
The energy loss is slow.

## Slide 83: Implicit Backward Euler’s Method Summary
The loss of energy caused by the numerical method is called “numerical damping”.
  DE solution methods that have numerical damping are usually very stable.
  The step size can be chosen for accuracy rather than for stability.
  Accuracy is low but stability is high if the time steps are too large.
  The implicit backward Euler method
  has very high numerical damping.

## Slide 84
There are numerical methods that have user-adjustable numerical damping.
  Implicit methods with adjustable numerical damping are very useful for MBD.
  They allow for the user to tune the amount of damping, but are very stable.

## Slide 85: The Newmark Method
The Newmark method is a common, simple method with tunable numerical damping.
  RecurDyn’s DE solver is very similar to the Newmark method.
    RecurDyn uses the Generalized-α method.
  The Newmark method is a 2nd order DE solver.
    Originally designed for solving dynamics problems in linear finite elements.

## Slide 86: The Newmark Method
Newmark method details
  There are 2 tunable parameters: β and γ
  Usually, the ranges of are specified as
    0 ≤ β ≤ 1/2
    0 ≤ γ ≤ 1
A quadratic equation
Use the form of g() that contains ÿ.

## Slide 87: The Newmark Method
The Newmark method is usually used as an implicit method.
  If β ≠ 0 or γ ≠ 0, then the method is implicit.
  Usually, we use the range
    1/4 ≤ β ≤ 1/2
    1/2 ≤ γ ≤ 1

## Slide 88: The Newmark Method with the 1 DOF Oscillator
The Newmark method with β = 1/4 and γ = 1/2,
  Becomes the implicit trapezoidal method.
    This has neutral stability.
      There is no numerical damping.
    The 1 DOF oscillator preserves energy perfectly, regardless of time step size.
h = 0.5
h = 0.01

## Slide 89: The Newmark Method with the 1 DOF Oscillator
The Newmark method with β = 1/2 and γ = 1,
  Becomes similar to the implicit backwards Euler method.
    Energy is lost quickly.
    But unconditionally stable.
    Time step size can be chosen for accuracy without considering stability.
h = 0.5
h = 0.01

## Slide 90: Solving an Implicit Newmark Time Step
Implementing the Newmark method
  There is only 1 independent function. We choose it to be yi+1.
  Use the first 2 equations to make ẏi+1 and ÿi+1 be functions of yi+1.
where

## Slide 91: Solving an Implicit Newmark Time Step
Implementing the Newmark method
  Then use the last equation as the Newton residual
  and solve r(yi+1) = 0 using Newton’s method.

## Slide 92: Solving an Implicit Newmark Time Step
Implementing the Newmark method
  The Jacobian of r(yi+1) is
  Where and are used to find:
and

## Slide 93: Solving MBD DEs
Solving the MBD equations of motion
  The MBD equations of motion
    Are DEs.
    But not simple DEs.
    They are “differential algebraic equations” (DAEs).
    They can be solved with the previously shown methods.
    But there are some extra details required.

## Slide 94: MBD DAEs
Differential Algebraic Equations (DAEs)
  The algebraic equations are usually either
    or
Differential equations
Algebraic equations

## Slide 95: DAEs Require Modifications to Solve
Solving the MBD DAEs with the previous solvers requires modifications to either the equations of motion or to the numerical method.
A problem occurs if no modifications are made.
  With no modification, the solution method would be:
    Use
    to get q̈ . The values of λ can be ignored.
  Then use q̈ in one of the DE solution methods previously shown.

## Slide 96: Constraint Drift if No Modifications Used
If the DE solution method was exact, then the method on the previous slide would be adequate.
But all DE solutions have error.
  The error in q would cause the constraints to be violated.
  Constraints violated: φ ≠ 0
    The bodies drift apart.
Initial config (t = 0)
Bodies drift apart (t > 0)
φ = 0
φ ≠ 0
Notes: =

## Slide 97: Strategies to Prevent Constraint Violation
MBD theory requires that φ = 0 always.
  So a strategy is required to enforce this.
2 common strategies:
  Modify the DAE equations of motion and use an implicit DE solver (for example, Newmark or Generalized-α)
    RecurDyn uses this method.
    This is the most common method.
  Coordinate partitioning

## Slide 98: Modifying the DAEs for Implicit DE Solvers
The equations of motion can be modified to allow implicit solvers to enforce φ = 0 directly.
  This means modifying g(t, q, q̇, q̈) = 0.
  Note that for MBD, g is a DAE.

## Slide 99: Modifying the DAEs for an Implicit Solver
The acceleration version of g, which would be used for unmodified DE solvers, is:
For implicit DE solvers, the constraint equations are used directly in g.
φ

## Slide 100: The Newmark Method for DAEs of MBD
The resulting set of equations to solve the MBD DAEs with the Newmark method are
  These equations directly find λi+1 values enforce φ = 0 at ti+1.

## Slide 101: Solving the Newmark Time Step
Solving a single MBD time step using the Newmark method with the modified DAEs
  Identical to the DE Newmark method.
where

## Slide 102: Solving the Newmark Time Step
Solving a single MBD time step using the modified Newmark method
  r uses the modified g
  where g is

## Slide 103: Solving the Newmark Time Step
This is solved with a Newton-Raphson loop.
    “Raphson” means that this is Newton’s method used to solve a system of equations.
  Find r(qi+1) = 0 iteratively using
where the chain rule of differentiation produces
and

## Slide 104: Numerical Damping for Implicit DAE Solutions
Numerical damping is required for implicit solutions to DAEs.
  If numerical damping is not used, the solution is unstable.
  The amount of numerical damping required depends on the problem.

## Slide 105: RecurDyn Simulation Execution
RecurDyn executes a simulation in a specific manner.
  Fundamentally, that process has 2 main parts:
    Initialization
    Stepping
Initialize model & solver
Step t from t0 to tend

## Slide 106: RecurDyn Simulation Execution
Initialize model and solver:
Read Model Input
Eliminate redundant φ
Find q0, q̇0, q̈0
qi = q0
q̇i = q̇0
q̈i =t q̈0
t = 0

## Slide 107: RecurDyn Simulation Execution
Step t from t0 to tend
  Each step is solved with Newton’s method.
Get rj
qi+1j+1 = qi+1j - rj*(r,qj)-1
Get r,qj
Update q̇i+1, q̈i+1,
qi+1 = qi, q̇i+1 = q̇i, q̈i+1 = q̈i, ti+1 = ti + h
|rj| <= tol?
qi = qi+1, q̇i = q̇i+1, q̈i = q̈i+1, ti = ti+1
Yes
No
if accuracy high, increase h
accuracy low?
Reduce h
No
Yes
ti >= tend?
Yes
No
Done
if ti is output time, generate output

## Slide 108: RecurDyn Simulation Execution
Getting rj and r,qj are the most complex parts of the execution.
  Computing rj involves:
rr = Mrqr+φ,qT λr-fre-fro
rφ = φ
rf = Mfqf+φ,qT λf-ffe-ffo
Evaluate all elastic and external forces:
gravity, contact, springs, finite element, user-defined, …
Combine all parts of r

## Slide 109: Thank You